.rm 65
.cw 12
.ul on
.op
.mt 4
.mb 7
.lh 8
.lq off
.ps off
.po 8
.sr 3
.cw 10
4.3  CONTROL ASSEMBLY A2
.fo ABW 9-14-90 ch4.doc
.he CHAPTER 4                Theory of Operation                            Page #

The  Control Board (Assembly A2) is a microprocessor based  sub-assembly  that �
contains all Modem Board (Assembly A3) filter frequency synthesizers, the AFSK �
transmit tone synthesizer, control bit latches, and the front panel  interface �
circuits.   In  addition,  the  Transmit Data (TXD)  and  Receive  data  (RXD) �
polarity,  regeneration, and receive clock recovery circuits are  included  on �
this board.  

The  following  sections contain detailed descriptions of  the  Control  Board �
circuit  illustrated  in Figures A1806 to A1827.  Please refer  to  the  block �
diagram in Figure 4.11 and the schematic diagrams during this discussion.


4.3.1 Microprocessor Controller

The  ST-8000A  Control  Board  (Assembly A2)  uses  a  conventional  dedicated �
microprocessor  architecture  with 32K bytes of read only (EPROM)  memory  for �
firmware  storage,  2K  bytes  of read/write (RAM) memory,  and  2K  bytes  of �
electrically alterable (EEPROM) memory.  The Z80A microprocessor uses a 4.9152 �
MHz  clock (PCLK) generated by a TTL crystal oscillator.  The 330  ohm  pullup �
resistor on U15-6 ensures that the clock signal meets the minimum high voltage �
level requirements of the Z80A.  The Control Board uses both memory mapped and �
I/O  port  mapped peripheral devices and latches.  The Z80A operates  with  no �
wait states.

Note the 10K ohm pullup resistors on the microprocessor write, WRM_L (U15-22), �
and read, RDM_L (U15-21), control signals.  These resistors hold these control �
lines  high when the processor is in the power on reset condition since  these �
control  lines  are  in a high impedance tri-state  condition  at  that  time.  �
Without  the pullup resistors, a false memory write signal might  corrupt  the �
parameters stored in the non-volatile parameter storage memory (U2).

The  Z80A  has two maskable interrupt sources: the serial  channel  controller �
interrupt,  INT_L (U56-12), and the front panel keypad interrupt, KBINT  (U64-�
1).  These two interrupt sources are combined by a 2 input NAND gate (U56)  to �
produce a common interrupt signal to drive the microprocessor interrupt  input �
(U15-16).  The front panel interrupt signal, KBINT, must be inverted since  it �
is  an active high signal.  When an interrupt occurs, the microprocessor  must �
poll  both  the serial controller (U66) shown in Figure A1815  and  the  front �
panel controller to see which device requested the interrupt.

The non-maskable interrupt, NMI (U15-17), provides a real time clock reference �
for  correctly  calculating ST-8000A timing delays.  This square  wave  timing �
signal is generated by the programmable timer (U1) in Figure A1807, and it  is �
set for a 0.5 ms period.  

The  RESET  (U9-5)  and  RESET_L (U9-6, U15-26) signals  are  generated  by  a �
"deadman"  timer  and  power on reset circuit (U9).   During  normal  ST-8000A �
operation,  the  deadman timer reset signal, SANITY_L (U9-7),  is  pulsed  low �
periodically by the microprocessor.  Should some abnormal situation cause  the �
microprocessor  to  cease operation, the deadman timer will force  a  hardware �
reset of the ST-8000A.  When a reset occurs, the RESET and RESET_L outputs are �
pulsed low and high, respectively, for approximately 0.25 seconds.
ŠDue  to the number of latches and devices on the control board, the Z80A  read �
and  write control signals are buffered by two buffer gates to  generate  RD_L �
(U10-8)  and WR_L (U10-11), respectively.  Note that the  un-buffered  signals �
RDM_L  and WRM_L are connected directly to the EPROM (U4), the RAM  (U3),  and �
the EEPROM (U2).


4.3.2  System Clocks

A  programmable timer (U1) in Figure A1807 generates the  reference  frequency �
for  all  of the frequency synthesizers, CKREF (U1-10), the  low  pass  filter �
clock,  LPCLK (U1-13), and the microprocessor real time reference  clock,  NMI �
(U1-17).   

All  of the ST-8000A frequency synthesizers are referenced to the same  4.9152 �
MHz  crystal oscillator that drives the microprocessor clock, PCLK  (U1-9,15).  �
One  16  bit programmable timer divides PCLK by 6 to generate the  819,200  Hz �
reference clock, CKREF (U1-10), used by all filter synthesizers.  In addition, �
the 4.9152 MHz clock is divided by various constants to generate the low  pass �
filter  clock,  LPCLK (U1-13), for the modem board.  An  inverting  buffer  is �
provided on CKREF to increase the fan-out capability.

A  separate  6.144 MHz oscillator reference is used for the NMI  clock.   This �
clock is divided by 3072 to produce a 2000 Hz square wave signal, NMI (U1-17), �
for  the 0.5 ms real time clock.  Note that the NMI signal is  disabled  until �
the NMI control signal, NMIENA (U1-16) is set high.

The  block  diagram in Figure 4.12 identifies the  significant  Control  Board �
(Assembly A2) clock signals.


4.3.3 Memory and I/O Address Map

The  microprocessor memory is divided into memory mapped and I/O  port  mapped �
sections.  All memory and I/O port address decoding is illustrated in  Figures �
A1806 and A1807.  

Decoding for the firmware memory (U4) is illustrated in Figure A1806.   Memory �
address bit 15, A15 (U15-5), and memory request, MREQ_L (U15-19) are  combined �
by a two input OR gate (U10) to generate the EPROM chip select signal  (U4-20) �
when both signals are low.

Except  for  the  firmware  memory chip select, all  memory  and  I/O  address �
decoding  is  contained in Figure A1807.  A 3-to-8 line decoder (U11)  is  the �
primary memory mapped device decoder, and it is enabled by the combination  of �
address bit 15, A15 (U11-6), high and memory request, MREQ_L (U11-5), low.   A �
second  address decoder (U12) provides additional decoding for  several  write �
only  latches  when it is enabled by write, WR_L (U12-4), low and  one  memory �
address select line (U11-13) low.

The  I/O  port mapped devices are decoded by two 3-to-8  line  decoders  (U13, �
U14).   The devices on the first decoder (U13) are both I/O input  and  output �
peripheral devices while those on the second decoder (U14) are I/O output only �
latched registers.
ŠThe  memory and I/O address map for the ST-8000A control board  is  summarized �
below (all addresses are shown in HEX format):


MEMORY MAPPED ADDRESSES

ADDRESS         DESCRIPTION                                    R/W      
--------------  ---------------------------------------------  ----------
0000H - 7FFFH   U4-20    27256 EPROM for firmware storage      READ
8000H - 87FFH   U3-18    2K x 8 RAM for temporary storage      READ/WRITE
8800H - 8FFFH   U2-18    2K x 8 EEPROM for parameter storage   READ/WRITE
A000H - A007H   U12-5    Synthesizer latches                   WRITE
 A000H           U41-11   MARK transmit tone, low byte         WRITE
 A001H           U43-11   MARK transmit tone, high byte        WRITE
 A002H           U40-11   SPACE transmit tone, low byte        WRITE
 A003H           U42-11   SPACE transmit tone, high byte       WRITE
 A004H           U45-11   MARK filter synthesizer, low byte    WRITE
 A005H           U46-11   MARK filter synthesizer, high byte   WRITE
 A006H           U49-11   SPACE filter synthesizer, low byte   WRITE
 A007H           U50-11   SPACE filter synthesizer, high byte  WRITE
E000H           U5-1,19  Transmit delay switch SW1             READ
E800H           U6-1,19  Transmit delay switch SW2             READ


I/O PORT MAPPED ADDRESSES

PORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
00H        U66-33    Serial controller                      INPUT/OUTPUT
08H    
10H        J8-12     Front Panel select (FP_L)              INPUT/OUTPUT
18H        U1-21     Programmable timer                     INPUT/OUTPUT
20H        U8-1,19   Unit Address switch SW4                INPUT
28H        U7-1,19   Remote Port rate switch SW3            INPUT
30H        U44-1,19  AMHO, level, RS232/MIL, KBINT, TXD     INPUT
38H - 3FH  U14-5     Misc. control latches                  OUTPUT
 38H        U47-11    MARK and SPACE filter Q latch         OUTPUT
 39H        U48-11    NMI, Regen, RX/TX control latch       OUTPUT
 3AH        U51-11    AMHC, Det. Mode, Channel, Mute, BIT   OUTPUT 
 3BH        U9-7      Sanity timer                          OUTPUT
 3CH        J8-13     Front panel LED latch 0 (LED0_L)      OUTPUT
 3DH        J8-14     Front panel LED latch 1 (LED1_L)      OUTPUT
 3EH        U52-11    High speed RX synthesizer, low byte   OUTPUT
 3FH        U53-11    High speed RX synthesizer, high byte  OUTPUT


4.3.4  EPROM, EEPROM, and RAM Memory

The ST-8000A memory address map is summarized below:

MEMORY ADDRESSES

ADDRESS         DESCRIPTION                                    R/W      
--------------  ---------------------------------------------  ----------
0000H - 7FFFH   U4-20    27256 EPROM for firmware storage      READŠ8000H - 87FFH   U3-18    2K x 8 RAM for temporary storage      READ/WRITE
8800H - 8FFFH   U2-18    2K x 8 EEPROM for parameter storage   READ/WRITE


Figure  A1806 illustrates the firmware EPROM (U4), the non-volatile  parameter �
EEPROM (U2), and the 2k x 8 RAM memory (U3).  The ST-8000A firmware is  loaded �
in  an industry standard 32k x 8 byte EPROM with 250 ns access time.  In  this �
unit, address bit 15, A15 (U15-5) selects either the EPROM when A15 is low  or �
the  EEPROM  and RAM when A15 is high.  Note that the memory  request  signal, �
MREQ_L (U15-19) enables memory decoding only during memory access cycles,  not �
during  I/O port access cycles.  The microprocessor read signal,  RDM_L  (U15-�
21), is connected directly to the EPROM (U4-22), RAM (U3-20), and EEPROM  (U2-�
20) output enable inputs.  The microprocessor write signal, WRM_L (U15-22), is �
connected to the RAM write input (U3-21) and the EEPROM write input (U2-21).


4.3.5  Memory Mapped Latches and Buffers

The  ST-8000A  controls the MARK and SPACE transmit tone and  bandpass  filter �
synthesizers  through memory mapped latches.  In addition, the transmit  delay �
time  switch setting is read from memory mapped switch buffers.  These  buffer �
addresses are summarized below:


MEMORY MAPPED LATCHES AND BUFFERS

ADDRESS         DESCRIPTION                                    R/W      
--------------  ---------------------------------------------  ----------
A000H - A007H   U12-5    Synthesizer latches                   WRITE
 A000H           U41-11   MARK transmit tone, low byte         WRITE
 A001H           U43-11   MARK transmit tone, high byte        WRITE
 A002H           U40-11   SPACE transmit tone, low byte        WRITE
 A003H           U42-11   SPACE transmit tone, high byte       WRITE
 A004H           U45-11   MARK filter synthesizer, low byte    WRITE
 A005H           U46-11   MARK filter synthesizer, high byte   WRITE
 A006H           U49-11   SPACE filter synthesizer, low byte   WRITE
 A007H           U50-11   SPACE filter synthesizer, high byte  WRITE
E000H           U5-1,19  Transmit delay switch SW1             READ
E800H           U6-1,19  Transmit delay switch SW2             READ


Each  of the synthesizers requires a 16 bit constant to set the output  square �
wave  frequency.  A detailed description of these registers is presented in  a �
subsequent  section and only the memory addresses are listed here.  

Two  other modem square wave signals are generated on the control  board;  the �
high  speed synthesizer, HSCLK (U23-19), and the low pass filter clock,  LPCLK �
(U64-12).   The  HSCLK synthesizer uses I/O mapped latches while  LPCLK  is  a �
square wave signal generated by the on board programmable timer (U1).

The  ST-8000A  reads  the  transmit delay setting as a 16  bit  value  set  by �
switches  SW1  and SW2 in Figure A1810.  For both switches, the  OPEN  or  OFF �
position is read as a TTL 1 or high signal while CLOSED or ON is read as TTL 0 �
or low signal.
Š
4.3.6  I/O Mapped Peripherals

The  ST-8000A  uses  I/O input and output  addresses  for  several  peripheral �
devices and control bit latches.  An I/O memory map is shown below:


I/O PORT MAPPED ADDRESSES

PORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
00H        U66-33    Serial controller - Regen control      INPUT/OUTPUT
01H        U66-33    Serial controller - Regen data         INPUT/OUTPUT
02H        U66-33    Serial controller - Remote control     INPUT/OUTPUT
03H        U66-33    Serial controller - Remote data        INPUT/OUTPUT

10H        J8-12     Front Panel controller - data          INPUT/OUTPUT
11H        J8-12     Front Panel controller - control       INPUT/OUTPUT

18H        U1-21     Programmable timer - CKREF clock       INPUT/OUTPUT
19H        U1-21     Programmable timer - LPCLK clock       INPUT/OUTPUT
1AH        U1-21     Programmable timer - NMI clock         INPUT/OUTPUT
1BH        U1-21     Programmable timer - control register  INPUT/OUTPUT

20H        U8-1,19   Unit Address switch SW4                INPUT
28H        U7-1,19   Remote Port rate switch SW3            INPUT
30H        U44-1,19  AMHO, level, RS232/MIL, KBINT, TXD     INPUT
38H        U47-11    MARK and SPACE filter Q latch          OUTPUT
39H        U48-11    NMI, Regen, RX/TX control latch        OUTPUT
3AH        U51-11    AMHC, Det. Mode, Channel, Mute, BIT    OUTPUT 
3BH        U9-7      Sanity timer                           OUTPUT
3CH        J8-13     Front panel LED latch 0 (LED0_L)       OUTPUT
3DH        J8-14     Front panel LED latch 1 (LED1_L)       OUTPUT
3EH        U52-11    High speed RX synthesizer, low byte    OUTPUT
3FH        U53-11    High speed RX synthesizer, high byte   OUTPUT


Figure  A1815  illustrates the dual channel serial controller (U66)  used  for �
receive data regeneration and the remote control port.  This serial controller �
contains internal baud rate generators to independently set the data rate  for �
the  remote  control  port  and receive data  regeneration.   For  a  detailed �
description  of  the  regeneration circuit and  remote  control  circuit,  see �
Section x.x.x.

The front panel controller is a programmable keyboard/display interface device �
described  in  a  subsequent  section.  For this  discussion,  note  that  the �
interface requires two I/O addresses; one for control and the other for data.

The  programmable  timer,  U1, in Figure A1807, contains  three  16  dividers.  �
These  registers  are  loaded  at the I/O addresses shown  above  to  set  the �
selected  low pass filter cutoff frequency, LPCLK (U1-13), and the  two  fixed �
rate clocks: NMI_L (U1-01) and CKREF (U64-12).

The  remaining  I/O address assignments control  various  operational  latched �
output bits.  The sections below detail each of these registers.Š

4.3.6.1  UNIT ADDRESS and REMOTE PORT RATE

PORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
20H        U8-1,19   Unit Address switch SW4                INPUT
28H        U7-1,19   Remote Port rate switch SW3            INPUT

The Unit Address switch, SW4 in Figure A1809, sets the ST-8000A unit  address.  �
This register is an 8 bit, read only input.

The  remote port rate switch, SW3 in Figure A1809, selects the data  rate  for �
the remote control port.  This registers is an 8 bit, read only input.


4.3.6.2  RECEIVE SIGNAL LEVEL and STATUS BITS

PORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
30H        U44-1,19  AMHO, level, RS232/MIL, KBINT, TXD     INPUT

The  microprocessor  can read the audio level of the receive  signal  and  the �
Automatic Mark Hold condition with an I/O mapped buffer shown in Figure A1808.  �
In   addition,  this  register  contains  the  state  of  the  transmit   data �
RS232/MIL188  option  jumper  setting in Figure A1816,  and  the  remote  port �
RS232/MIL188 option jumper setting in Figure A1815.

The state of KBINT (U64-2) in Figure A1806 is also provided in this  register.  �
Since two different interrupt sources are combined in a single  microprocessor �
interrupt signal, this register may be read to see whether the interrupt  came �
from the front panel keyboard/display controller.

The state of the TXD input may be read in this register as well.

The bit assignments in this register are shown below:


Input: LEVEL_L

BIT  PIN     DESCRIPTION
---  ------  --------------------------------------------------------------
 0   U44-4   J7-23  Automatic Mark Hold (AMHO):  1 = LOS, 0 = SIGNAL
 1   U44-17  J7-20  AGC Gain A (DGA)
 2   U44-2   J7-21  AGC Gain B (DGB)
 3   U44-6   J7-22  AGC Gain C (DGC)
 4   U44-11  U64-2  Front Panel controller Interrupt (KBINT'): 0 = intr req
 5   U44-15  J2SW   Transmit Data RS232/MIL188: 1 = MIL188, 0 = RS232
 6   U44-8   J5SW   Remote Port RS232/MIL188:   1 = MIL188, 0 = RS232
 7   U44-13  U59-3  Transmit Data input (TXD'): 1 = MARK, 0 = SPACE



4.3.6.3  MARK/SPACE BANDPASS FILTER Q
ŠPORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
38H        U47-11    MARK and SPACE filter Q latch          OUTPUT

The  Q's of the MARK and SPACE input filters on the modem board  are  selected �
with latched control bits on the Control Board.  Since each filter requires  4 �
bits, a single 8 bit latch is used as shown in Figure A1808.


Output: OUT0_L

PIN       DESCRIPTION                      
--------  -----------------------------------------
U47-2     MARK Filter Q High/Low           to J7-15
U47-5     MARK Filter Q bit 3              to J7-14
U47-6     MARK Filter Q bit 2              to J7-13
U47-9     MARK Filter Q bit 1              to J7-12
U47-12    SPACE Filter Q High/Low          to J7-19
U47-15    SPACE Filter Q bit 3             to J7-18
U47-16    SPACE Filter Q bit 2             to J7-17
U47-19    SPACE Filter Q bit 1             to J7-16

The Q values selected with these control bits are listed in Table 4.2.


4.3.6.4  CONTROL REGISTER 1

PORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
39H        U48-11    NMI, Regen, RX/TX control latch        OUTPUT

Several  miscellaneous  control signals are latched in an octal  D-type  latch �
(U48) shown in Figure A1808.  This latch contains a reset input, RESET_L (U48-�
1),  that will force all of the control signals to a low state when the  power �
is  first turned ON.  This reset ensures that the NMI control  signal,  NMIENA �
(U48-2), signal is low during power on initialization.

The function of each control signal is summarized below:


Output: OUT1_L, BIT 7

PIN       DESCRIPTION                      
--------  -----------------------------------------
U48-2     NMI Enable bit (NMIENA)          to U1-16

The NMI Enable bit (NMIENA) activates the NMI real time clock in Figure  A1807 �
for the microprocessor.  A high signal enables NMI (NMIENA = 1).  When a reset �
occurs, this bit is forced low to disable NMI (NMIENA = 0).


Output: OUT1_L, BIT 6

PIN       DESCRIPTION                      
--------  ------------------------------------------------ŠU48-5     REGEN Enable (REGEN)             to U63-5, U64-5

The  Regeneration Enable bit (REGEN) determines whether the data terminal  RXD �
output in Figure A1816 is connected to the demodulated RX data from the  modem �
or  to the control board regeneration serial controller.   When   regeneration �
mode is disabled (REGEN = 0), the modem receive data signal, RXDTR (U57-2), is �
connected  to  the modem terminal receive data output, RXDFR  (U63-11).   When �
regeneration  is  enabled  (REGEN  = 1) the  modem  receive  data,  RXDTR,  is �
connected to the regeneration serial controller receive data input, RXDB (U66-�
27)  and the regenerated data from the transmit data output, TXDB (U66-25)  is �
connected  to  the modem terminal data connector receive data  output,  RXDFR.  �
For regeneration to work properly, the correct data rate and word length  must �
be programmed into the serial controller channel B.


Output: OUT1_L, BIT 5

PIN       DESCRIPTION                      
--------  --------------------------------------------------------
U48-6     Resync RXD (RSYNC)               to U64-11, U56-1, U65-2

The ST-8000A has the ability to resynchronize the receive data, RXDTR,  signal �
to  a recovered receive data clock.  D-latch U55 in Figure A1816  samples  the �
RXDTR  signal from the modem  and re-clocks this data with a  stable  internal �
data  rate clock.  The result of this resynchronizing operation is  to  reduce �
the  jitter  in the data terminal receive data output, RXDFR  (U63-11).   When �
enabled (RSYNC = 1) the receive data is resynchronized.  When disabled  (RSYNC �
= 0) receive data is passed to the data terminal without re-clocking.


Output: OUT1_L, BIT 4

PIN       DESCRIPTION                      
--------  -----------------------------------------
U48-9     RXD Normal/Reverse  (RXDNR)      to U57-1

The  ST-8000A  provides  independent control over transmit  and  receive  data �
polarity, as shown in Figure A1816.  When set for NORMAL receive data (RXDNR = �
0),  RXDTR  from the modem is passed through to RXDB (U57-3)  without  change.  �
When enabled (RXDNR = 1) the RXDTR signal from the modem is inverted before it �
reaches RXDB (U57-3).


Output: OUT1_L, BIT 3

PIN       DESCRIPTION                      
--------  -----------------------------------------
U48-12    TXD Normal/Reverse  (TXDNR)      to U57-4

The  ST-8000A  provides  independent control over transmit  and  receive  data �
polarity, as shown in Figure A1816.  When set for NORMAL transmit data  (TXDNR �
=  0), TXDIN from the modem is passed through to TXD (U57-6)  without  change.  �
When enabled (TXDNR = 1) the TXDIN signal from the modem is inverted before it �
reaches TXD.
Š
Output: OUT1_L, BIT 2

PIN       DESCRIPTION                      
--------  -----------------------------------------
U48-15    TXD Enable (TXENABLE)            to U56-10

The  ST-8000A  Built  In Tests (BIT) require that the external  TXD  input  be �
disabled during testing.  When disabled (TXENABLE = 0) the data terminal TXDIN �
input  is  blocked at U56-8.  When enabled (TXENABLE = 1)  the  data  terminal �
TXDIN input is connected to the TXD (U57-6) output.


Output: OUT1_L, BIT 1

PIN       DESCRIPTION                      
--------  -----------------------------------------
U48-16    [not assigned]


Output: OUT1_L, BIT 0

PIN       DESCRIPTION                      
--------  -----------------------------------------
U48-19    Diversity Enable  (DIVC)         to J7-25

If  the  diversity  option is installed in the  ST-8000A,  diversity  mode  is �
enabled when this signal is high (DIVC = 1) and disabled otherwise.


4.3.6.5  CONTROL REGISTER 2

PORT       DESCRIPTION                                      I/O
---------  -----------------------------------------------  ----------
3AH        U51-11    AMHC, Det. Mode, Channel, Mute, BIT    OUTPUT 

Several  miscellaneous  control signals are latched in an octal  D-type  latch �
(U51)  shown in Figure A1808.  All of these control signals are passed to  the �
modem board.

The function of each control signal is summarized below:


Output: OUT2_L, BIT 7

PIN       DESCRIPTION                      
--------  ------------------------------------------
U51-2     Automatic Mark Hold Enable (AMHC) to J7-24

The  Automatic  Mark Hold Enable signal (AMHC) enables and  disables  the  AMH �
circuit  on the modem board.  The automatic mark hold feature is enabled  when �
AMHC = 1 and is disabled when AMHC = 0.


Output: OUT2_L, BIT 6Š
PIN       DESCRIPTION                      
--------  -----------------------------------------
U51-5     High Speed Enable (HSLS)         to J7-26

The  High Speed Enable selects the low or high speed demodulator on the  modem �
card.   The  high speed demodulator is enabled when HSLS = 1 and  is  disabled �
when HSLS = 0.


Output: OUT2_L, BIT 5,4

PIN       DESCRIPTION                      
--------  -----------------------------------------
U51-6     Detector Mode (DMA)              to J7-27
U51-9     Detector Mode (DMB)              to J7-28

The  detector mode is selected with these two bits.  The detector options  are �
listed below:

     B  A   Detector Mode
     -  -   -------------
     0  0   MARK/SPACE
     0  1   MARK ONLY
     1  0   SPACE ONLY
     1  1   MARK/SPACE = ATC.


Output: OUT2_L, BIT 3

PIN       DESCRIPTION                      
--------  -----------------------------------------
U51-12    Channel Select (CHSEL)           to J7-32

The  modem  board has two channels: the modulator and  the  demodulator.   The �
Channel Select control signal determines whether the transmit or receive tones �
are  displayed  on  the front panel bar graph displays.   The  demodulator  is �
selected  when CHSEL = 1, and the modulator channel is selected when CHSEL   = �
0.

Output: OUT2_L, BIT 2

PIN       DESCRIPTION                      
--------  -----------------------------------------
U51-15    Transmit Mute (MUTE)             to J7-33

The  Transmit  Mute signal enables and disables the output AFSK  tones.   When �
MUTE  =  0,  the transmit tones are enabled and the  radio  keyline  relay  is �
activated or closed.  When MUTE = 1, the transmit tones are disabled, and  the �
PTT relay is not activated.


Output: OUT2_L, BIT 1

PIN       DESCRIPTION                      Š--------  -----------------------------------------
U51-16    Loopback Enable (BCB)            to J7-36
U51-19    Loopback Enable (BCA)            to J7-34

The  Loopback enable control bits enable and disable an analog  loopback  that �
connects the AFSK output signal to the audio input.  Three different  loopback �
gain options are available:

     B  A   Loopback Gain
     -  -   ----------------
     0  0   Disabled
     0  1   0 dBm
     1  0   -20 dBm
     1  1   -40 dBm


4.3.7  MARK/SPACE Transmit Tone Generator

The  AFSK tone oscillator illustrated in Figure A1811 is a 16 bit  full  adder �
operating as a digital signal synthesizer with a square wave output set to  50 �
times  the audio tone frequency.  Two sets of latches store the constants  for �
the MARK and SPACE tones,  and the transmit data signal, TXD (U55-12), selects �
either the MARK tone (TXD = 0) or SPACE tone (TXD = 1).

The D-type latch is included to synchronize the changes between MARK and SPACE �
to that portion of the synthesized sine wave output where the slope is 0.   In �
this  fashion, the distortion is minimized.  The synchronizing signal,  FSKCLK �
(U55-11) pulses once per sine wave cycle.

The  MARK/SPACE  tone digital synthesizer is a 16 bit full  adder  implemented �
with four 4 bit full adders, U24 - U27.  On each rising edge of CKREF (U17-11, �
U16-11), a 819,000 Hz clock, the current 16 bit sum is latched into two D-type �
latches, (U16, U17).  These latch outputs are then added to the tone  constant �
stored  in either the MARK or SPACE tone latch depending on the state  of  the �
sampled  TXD  signal  (U55-9, U55-8).  When a MARK is  transmitted,  the  MARK �
constant  registers (U41, U43) are enabled on the adder inputs.  When a  SPACE �
is  transmitted,  the SPACE constant registers (U40, U42) are enabled  on  the �
adder  inputs.  The selected constant is summed with the previous sum  latched �
in U16 and U17 to form a new sum that will be latched on the next rising  edge �
of CKREF to complete the cycle.  The output of this synthesizer, TFSK (U17-19) �
has a nominal frequency of 50 times the selected tone frequency.  

Figure  4.13  summarizes  the digital frequency  synthesizer  operation.   The �
digital  synthesizers generate their output frequency through  addition.   The �
frequency is determined by the magnitude of the constant loaded into the input �
latches  and  the  clock reference frequency  driving  the  synthesizer.   For �
example,  if  a constant 001 hex is loaded into the MARK latch, and TXD  =  0, �
then the sum at the output of the latches U16 and U17 will be incremented by 1 �
count  for  each rising edge of CKREF.  After 32,768 rising  edges,  the  TFSK �
output will change from 0 to 1.  Then, after another 32,768 rising edges,  the �
TFSK  signal will change from 1 to 0.  The total time for one cycle is  65,536 �
clock  cycles of CKREF.  If CKREF is set to 819,200 Hz, the TFSK  output  will �
have  a frequency of 12.5 Hz.  If the MARK latch is changed to a  constant  of �
002 hex, then TFSK will equal 25 Hz.  The largest constant that can be  loaded �
into  the  MARK  register  is  32,767, and  the  resulting  output  signal  is �Šapproximately 409,587 Hz.  Thus, this synthesizer may be set to any  frequency �
between 12.5 Hz and 409,600 Hz in steps of 12.5 Hz.

At  low frequencies or when the constant is an exact divisor of  819,200,  the �
output  waveform  on  TFSK (U17-19) is nearly a 50% duty  cycle  square  wave.  �
However,  if the constant is not an integer divisor, the relationship  between �
the constant and CKREF generates signal jitter.  While this jitter is  visible �
on  an  oscilloscope, the resulting sine wave output is smoothed by  the  sine �
wave approximation process and the 50 times over sampling.

In  the ST-8000A the tone synthesizer generates output frequencies on TFSK  of �
15,000  Hz  and 150,000 Hz in steps of 25 Hz.  The resulting output  from  the �
AFSK generator on the modem card is 300 to 3000 Hz in 0.5 Hz increments.   For �
each  tone frequency, the constant loaded into the MARK and SPACE register  is �
calculated using the following formulae:

     MARK AFSK TONE CONSTANT  = MARK  TONE FREQUENCY * 4
     SPACE AFSK TONE CONSTANT = SPACE TONE FREQUENCY * 4

For  example, to transmit a MARK tone of 2125 Hz and a SPACE tone of 2295  Hz, �
the  MARK constant is 8,500 and the SPACE constant is 9,180.  The lowest  tone �
constant is 1,200 for 300 Hz, and the highest is 12,000 for 3000 Hz.


4.3.8  MARK Filter Synthesizer

The MARK filter synthesizer is illustrated in Figure A1812.  This  synthesizer �
generates  the clock, MCLK (U19-19), used to set the center frequency  of  the �
MARK  bandpass  filter  on  the modem board (J7-1).   The  operation  of  this �
synthesizer  is  identical to the transmit tone synthesizer described  in  the �
previous section, and the output of this synthesizer is 50 times the  selected �
MARK frequency.

The  MARK filter constant is loaded into two octal D-type latches (U45,  U46).  �
The  output frequency of the MARK filter synthesizer is calculated  using  the �
following formula:

     MARK FILTER CONSTANT = MARK TONE FREQUENCY * 4


4.3.9  SPACE Filter Synthesizer

The SPACE filter synthesizer is illustrated in Figure A1813.  This synthesizer �
generates  the clock, SCLK (U21-19), used to set the center frequency  of  the �
SPACE  bandpass  filter  on the modem board (J7-3).   The  operation  of  this �
synthesizer  is  identical to the transmit tone synthesizer described  in  the �
previous section, and the output of this synthesizer is 50 times the  selected �
SPACE frequency.

The SPACE filter constant is loaded into two octal D-type latches (U49,  U50).  �
The  output frequency of the SPACE filter synthesizer is calculated using  the �
following formula:

     SPACE FILTER CONSTANT = SPACE TONE FREQUENCY * 4
Š
4.3.10  HIGH SPEED Filter Synthesizer

The  HIGH  SPEED  filter synthesizer is illustrated  in  Figure  A1814.   This �
synthesizer  generates  the  clock, HSCLK (U23-19), used  to  set  the  center �
frequency  of the HIGH SPEED bandpass filter on the modem board  (J7-7).   The �
operation  of this synthesizer is identical to the transmit  tone  synthesizer �
described in the previous section, except that  the output of this synthesizer �
is set to the center frequency of the HIGH SPEED filter plus 10,000 Hz.

The  HIGH SPEED filter constant is loaded into two octal D-type latches  (U52, �
U53).  The output frequency of the HIGH SPEED filter synthesizer is calculated �
using the following formula:

     HIGH SPEED FILTER CONSTANT = ( CENTER FREQUENCY + 10,000 ) / 12.5


4.3.11  LOW PASS Filter Oscillator

The  LOW PASS filter oscillator controls the corner frequency of the low  pass �
filter  in  the detector of the modem board.  The programmable timer  (U1)  in �
Figure  A1807 generates this clock signal, LPCLK (U1-13), and it is passed  to �
the  filter  on the modem board (J7-5).  This oscillator is simply  a  16  bit �
counter  with a clock reference frequency of 4.9152 MHz.  The 16 bit  constant �
is loaded into the programmable timer.

For  a given data rate, the LOW PASS filter constant is calculated  using  the �
following formula:

     LOW PASS CONSTANT = ( 4,915,200 ) / ( 96 * DATA RATE )

This constant varies between 5,120 for 10 bits per second to 43 for 1200 bps.


4.3.12  Regeneration

Figure A1815 illustrates the serial channel controller (U66) used for  receive �
data  regeneration  and  the  remote control port.   This  controller  has  an �
internal baud rate clock that sets the data rate for both channels.  

When  regeneration is active (REGEN = 1) asynchronous characters  received  on �
the RXDB (U66-27) input of the serial controller are passed to the TXDB  (U66-�
25)  output.   Regeneration  generates each  receive  character  removing  any �
received  jitter  and  noise.  Note that regeneration is  only  possible  when �
receiving asynchronous start-stop characters with character lengths of 5 to  8 �
data bits.

The   serial   controller  operates  in  an  interrupt  driven   mode   during �
regeneration.  Any character received on the RSCB (U66-27) input causes  INT_L �
(U66-5)  to go low signaling a data available interrupt.   The  microprocessor �
controller reads the serial controller to clear this interrupt flag.

Note  that regeneration can only work properly when the data presented to  the �
RXDB  (U66-27)  input has polarity set such that a MARK equals  TTL  high  and �
SPACE  equals TTL low.  This should be the case when the MARK tone is set  for �Šthe  correct tone and the receive data normal/reverse, RXDNR (U57-1), are  set �
correctly  for the desired signal.  The regenerated signal on  RXDFR  (U63-11) �
will have MARK high and SPACE low independent of the RXDNR setting.

Whether  regeneration is enabled or not, a data rate clock equal to  16  times �
the  baud  rate  is  generated on the TXCLK  (U66-26)  output  of  the  serial �
controller.   This  clock  provides  a time reference  signal  for  the  clock �
recovery  circuit described in the next section.  The frequency of this  clock �
is set by the BAUD RATE setting on the front panel; it is set to 16 times that �
rate.


4.3.13  Remote Control Port

The dual channel serial controller (U66) channel A is connected to the  Remote �
Control port on the ST-8000A.  In Figure A1815, note that the polarity of  the �
data  on  this port may be set to RS232 or MIL188 levels with the  jumper  J5.  �
When  in  the RS232 position, J5SW low, the port has normal  RS-232  MARK  and �
SPACE control levels.

The  remote  port REMRXD is converted to TTL level (U59-6) and passed  to  the �
RXDA  input  on  the  serial controller (U66-13)  after  passing  through  the �
RS232/MIL188  polarity gate.  The ST-8000A may read the Clear to Send,  REMCTS �
(U59-8), to control output flow control.

The  remote  port  REMTXD signal comes from the TXDB (U66-15)  output  of  the �
serial  controller and the RS232/MIL188 polarity gate.  The REMTXD  signal  is �
combined  with the RTSA (U66-17) serial controller output so that this  signal �
is  held in the MARK hold state when RTSA is low.  Note that the  RTSA  output �
drives  the REMRTS (U62-8) signal on the remote control port.  In addition,  a �
REMDTR (U62-11) and REMCTS (U62-6) signals are provided.

The  remote  port is configured as a mult-drop output where up to  8  ST-8000A �
remote  port  transmit  data outputs, REMTXD, may be  connected  in  parallel.  �
Diodes D2 and D3 in Figure A1815 actively pull REMTXD to MARK and SPACE levels �
when RTSA (U66-17) is low or enabled, and allow the REMTXD to float when  RTSA �
is  high.  Thus, the output data line is connected only when this unit  has  a �
response  to  transmit.  The zener diodes D1 and D4 limit  the  REMTXD  output �
voltage  swing  to  MIL188 levels.  To improve noise immunity  on  the  common �
transmit  data output line, REMTXD, one and only one ST-8000A in a group of  2 �
or more units should have jumper J3 set to connect the resistor to the  output �
line.   This  resistor defaults the line to a MARK or negative  voltage  level �
when no unit is actively sending.


4.3.14  Synchronous Data Clocks

Figure  A1816  illustrates the receive data clock,  RXCLK  (U60-11),  recovery �
circuit for serial data received by the modem board.  Basically, this  circuit �
synchronizes an internal clock to the edges in the serial receive data,  RXDTR �
(U57-2), from the modem card.

Changes in the receive data signal generate pulses (U57-11) that reset a 4 bit �
counter  (U58) each time a change occurs.  This counter is driven by  a  clock �
running at 16 times the baud rate, TXCLKB (U58-1), and the output of the  most �Šsignificant bit of the counter (U58-6) will change after 8 TXCLKB cycles.   If �
this  clock is properly set, the clock transition occurs at the center of  the �
data  bit  and  a correct receive data recovered  clock,  RXCLK  (U60-11),  is �
generated.   Jumper  J4 selects either normal or inverted clock for  RS232  or �
MIL188 receive data.

A  D-type  latch  is driven by the recovered clock  (U55-3)  to  re-clock  the �
receive data (U55-5).  In some cases, re-clocking the data will reduce receive �
data  jitter and improve system performance.  Note that the receive  data  re-�
clocking latch will work with either synchronous or asynchronous receive  data �
since  it  does  not depend on a start or stop bit,  nor  does  data  polarity �
matter.

The  baud  rate  clock TXCLKB (U58-1) is simply divided by 16 in  a  four  bit �
counter (U58) to generate the TXCLK (U60-3) synchronous transmit clock.  Since �
the  transmit data input, TXDIN (U59-1), directly drives the  tone  generator, �
there  is no need to change this clock phase for RS232 and MIL188  data.   The �
ST-8000A transmits correctly in either case.