.rm 65
.cw 12
.ul on
.op
.mt 4
.mb 7
.lh 8
.lq off
.ps off
.po 8
.sr 3
.cw 10
4.4.3  Front Panel Controller
.fo ABW 9-16-90 ch4_fp.doc
.he CHAPTER 4                Theory of Operation                            Page #

The  ST-8000A uses an integrated keyboard decoder and display controller  (U8) �
shown in Figure A1819 to handle the front panel keypad input and seven segment �
display  outputs.   This  device  debounces  keypad  entries  to  prevent  the �
inadvertent  entry  of  multiple keys, and buffers the display  data  for  the �
multiplexed front panel numerical displays and indicators.

The  keypad/display  interface  controller (U8) is  an  8  bit  microprocessor �
peripheral device that connects directly to the control board data bus (DB0 to �
DB7), the read (RD_L) and write (WR_L) signals, address bit 0 (A0), the  front �
panel  enable (FP_L), and system reset (RESET).  The microprocessor reads  and �
writes  the control and data registers in this device to input keypad  entries �
and load the display buffer output registers.  An internal counter divides the �
system clock (PCLK) input to set the keypad and display scanning rate.

The keypad and the front panel display are scanned through the binary  encoded �
scan  line  outputs (SL0 to SL3) in Figure A1819 and 3-to-8 line  decoders  in �
Figures  A1820 and A1821.  Keypad entries are detected as a TTL low on one  of �
the row inputs (RL0 to RL3).

The seven segment display segment drivers are connected to the segment outputs �
(U8-24 to U8-31).  Data on this output bus is inverted; to turn a segment  ON, �
the corresponding output is held at a TTL low level when the digit is scanned.  �
Because the segment outputs do not have sufficient drive capability,  discrete �
PNP  switching transistors (Q17 to Q24) in Figure A1819 buffer  these  outputs �
for  all of the display segments.  The display segments anodes of  the  common �
cathode  seven segment display digits are all driven in parallel, as shown  in �
Figure A1822, and one scanned digit is selected with the digit driver  circuit �
in Figure A1821.


4.4.3  Keypad

The front panel keypad is a matrix of single pole momentary switches  arranged �
in three rows of 9 switches.  The low three bits of the scan line outputs (SL0 �
to SL2) drive a 3-to-8 line decoder (U7) to select one of 8 keypad columns  by �
forcing  that column select line low.  If any of the keypad switches  in  that �
column  are  closed, one of the row lines (RL0 to RL3) will be forced  low  to �
signal the keypad/display controller (U8) that a key has been pressed.

Note  that  the keypad is arranged as 4 rows of 8 keys and 1 row  of  3  keys.  �
This  keypad/display  controller (U8) has a maximum capacity of 8  rows  by  8 �
columns, so it cannot scan the 9 columns in a simple matrix fashion.  However, �
by  connecting three of the column drivers to the last column, and  connecting �
that  column to a fourth row line (RL3), the entire matrix of switches may  be �
scanned.

When a keypress is detected, the keypad/display controller (U8) stores the row �
and  column locations into a key buffer and interrupts the  microprocessor  by �
forcing the front panel interrupt line (KBINT) high.

ST-8000A  firmware  determines the function of all front  panel  keypad  keys; �
there are no hardwired switch functions.
Š
4.4.3  Numerical Displays

The  front panel assembly has 15 common cathode seven segment  display  digits �
and two additional LEDs driven in a multiplexed fashion by the  keypad/display �
controller  (U8).  The scan line outputs (SL0 to SL3) select one of  16  digit �
drivers using two 3-to-8 line decoders shown in Figure A1821.  For each of the �
16  scan line selections, a single common cathode digit driver  transistor  is �
enabled  through an inverting buffer.  As each digit is selected in turn,  the �
segments  are  turned  ON  that  correspond  to  the  data  presented  on  the �
keypad/display controller data output lines in Figure A1819.

The  keypad/display  controller (U8) is configured to scan  the  entire  front �
panel display every 20 ms or 50 times per second to avoid visual flicker.   In �
addition,  the keypad/display controller blanks the display as the scan  lines �
change so that display digit contrast is improved.

Figure  A1822  illustrates  the assignment of the digits to  the  front  panel �
locations.  Five digits are assigned to the MARK and SPACE frequency  windows, �
four  digits  to the BAUD window, and a single digit to the  CHANNEL  display.  �
The  two  LED's  mirror  the channel selection, but they  are  scanned  as  an �
independent digit during scan time slot 15.

The digit assignments for the front panel are summarized below:

     DISPLAY   DIGIT SCAN NUMBER
     --------  -----------------
     MARK      4   3   2   1   0
     SPACE     9   8   7   6   5
     BAUD         13  12  11  10
     CHANNEL                  14
     LED                      15


Each seven segment display digit has segments assigned as shown below:

               BIT
     SEGMENT   7  6  5  4  3  2  1  0
     -------   -  -  -  -  -  -  -  -                 a
     SEG dp    X                                    -----
     SEG g        X                              f |     | b
     SEG f           X                             |  g  |
     SEG e              X                           -----
     SEG d                 X                     e |     | c
     SEG c                    X                    |     |
     SEG b                       X                  -----   o dp
     SEG a                          X                 d


4.4.3  LED Indicators

In  addition  to  the multiplexed front panel display  digits,  there  are  16 �
latched front panel LED indicators illustrated in Figure A1823.  The two octal �
latches  (U1,  U2) are connected to the control board data bus (DB0  to  DB7).  �
The  signals to load the LED latches come directly from an I/O output  address �Šdecoder  on  the  control  board (LED0_L, LED1_L).   The  LED  latch  data  is �
inverted; a TTL 0 turns the corresponding LED ON.

The LED data bus bit assignments for the front panel are summarized below:


                  BIT
     LED0_L (U1)  7  6  5  4  3  2  1  0
     -----------  -  -  -  -  -  -  -  -
     MARK         X
     CENTER          X
     SPACE              X
     SHIFT                 X
     SYNC                     X
     FSK                         X
     MARK ONLY                      X
     SPACE ONLY                        X


                  BIT
     LED1_L (U2)  7  6  5  4  3  2  1  0
     -----------  -  -  -  -  -  -  -  -
     REGEN        X
     AMH             X
     HOLD               X
     REV                   X
     ENTER                    X
     DIV                         X
     MUTE                           X
     REMOTE                            X