.mt 4
.mb 7
.cw 12
.op
.ul on
.lh 8
.lq off
.ps off
.po 8
.sr 3
TO:       Bill Henry
          Gary Musgrave
FROM:     A.B. White
SUBJECT:  ST-8000A KEYPAD OPERATION
DATE:     December 23, 1990
.fo ABW 12/23/90 keypad2.doc
.he ST-8000A KEYPAD OPERATION                                  Page #


The ST-8000A keypad provides complete control over the  operation �
of  the ST-8000A modem.  It is used to set the MARK and SPACE  or �
CENTER and SHIFT frequencies for the demodulator (channel 1)  and �
the modulator (channel 2) as well as set various other parameters �
for both channels and activate built in test routines.

Whenever parameters are entered, the ENTER key indicator  flashes �
to  signal  the change.  To save this new parameter in  the  non-�
volatile memory, the user need only press the ENTER key.  At  any �
time  before  ENTER is pressed, the CLEAR key may be  pressed  to �
ignore the new setting and return the ST-8000A to the  previously �
saved parameters.

In  the  following sections, the function of each of  the  keypad �
function  keys is summarized.  The keys are presented  in  keypad �
order starting with the left hand column.


1.  NUMBER KEYS

The  number  keys,  0  to  9 and  0.5,  are  used  to  enter  new �
frequencies, baud rates, and regeneration word length, and select �
internal BIT tests.  The number keys are only active after one of �
the  following function keys has been pressed: MARK, SPACE,  BAUD �
RATE, or SYNC.  When entering a number, the corresponding display �
window  shows  the  new setting, but the  new  parameter  is  not �
activated  until the ENTER key is pressed.  If the CLEAR  key  is �
pressed  before  ENTER, the modem will return to  the  previously �
stored settings and will ignore the new setting.


2.  ENTER KEY

The ENTER key stores the current modem parameters in non-volatile �
memory and turns OFF the flashing ENTER indicator.  Pressing  any �
parameter key causes the ENTER indicator to flash.  If the  CLEAR �
key is pressed before ENTER, the modem returns to the  previously �
stored  parameters.   Note: the REMOTE key does not  require  the �
ENTER key.


3.  M/S  CENT KEY

The  M/S  key  determines the front panel display  mode  and  the �
parameter entry mode.  Pressing the M/S key turns ON the MARK and �
SPACE  indicators and displays the MARK and SPACE  filter  center �
frequencies  when  channel 1 is selected, or  the  transmit  tone �
frequencies  when channel 2 is selected.  In this mode, the  MARK �Šand  SPACE keys set the MARK and SPACE frequencies directly  for  �
the selected channel.

Pressing 2ND then M/S changes the front panel display to show the �
CENTER and SHIFT frequencies for either channel 1 or 2.  In  this �
mode,  the  indicators next to the CENTER and  SHIFT  labels  are �
turned ON.  In addition, the MARK and SPACE keys load the  CENTER �
and SHIFT frequencies, respectively, for the selected channel.

To  save the new display and parameter entry mode, the ENTER  key �
must be pressed.


4.  BIT KEY

The  BIT routines are activated by pressing 2ND the BIT  followed �
by  ENTER or a number and ENTER.  If ENTER alone is pressed,  the �
complete BIT procedure is performed.  The table below  summarizes �
the  available test features and the corresponding  BAUD  display �
message.


     KEY       DESCRIPTION                        BAUD DISPLAY
     -----     ---------------------------------  ------------
     ENTER     Automatic BIT procedure             -
     1         Automatic BIT procedure             -
     2         Constant MARK                       "_---"
     3         Constant SPACE                      "-___"
     4         Alternating MARK/SPACE at TX BAUD   "Alt "
     7         Internal Loopback at 0 dBm          "LP 1"
     8         Internal Loopback at -20 dBm        "LP 2"
     9         Internal Loopback at -40 dBm        "LP 3"


5.  2ND KEY

The 2ND key accesses the second level functions on certain  keys.  �
The  ST-8000A  has second level functions only on  the  following �
keys:  M/S CENT, BIT, MARK ONLY, SPACE ONLY, AMH HOLD, NORM  REV, �
and SYNCH REGEN.  Pressing any key other than those listed  above �
returns the keypad to first level functions.

.pa
6.  FSK KEY

The  FSK  key is used with MARK ONLY and SPACE ONLY  to  set  the �
demodulator  discriminator mode.  Pressing FSK turns ON  the  FSK �
indicator  and selects the MARK/SPACE discriminator  mode.   This �
key is functional whether channel 1 or channel 2 is selected.

    KEYS       ACTION
    -----      -------------------------------------------------
    FSK        Select demodulator MARK/SPACE mode.
               Turns ON the FSK indicator.

To save the new demodulator mode, the ENTER key must be pressed.


7.  MARK ONLY KEY

The MARK ONLY key has both a first and a second level function.

7.1  MARK (first level):

Press  MARK alone to enter the MARK filter frequency (channel  1) �
or the MARK transmit tone (channel 2) when the MARK/SPACE display �
mode   is  active.   The  following  example  assumes  that   the �
demodulator, channel 1, is selected.

    KEYS       ACTION
    -----      -------------------------------------------------
    MARK       Blank the MARK display window, ENTER turns ON
    2125       "2125.0" shows in the MARK window
    ENTER      "2125.0" flashes, ENTER turns OFF
               The MARK filter is set to 2125.0 Hz


When the display mode is set for CENTER/SHIFT, the MARK key  sets �
a new CENTER frequency for the demodulator filters, channel 1, or �
the  transmit  tones, channel 2.  The following  example  assumes �
that the demodulator, channel 1, is selected.

    KEYS       ACTION
    -----      -------------------------------------------------
    MARK       Blank the CENTER display window, ENTER turns ON
    2210       "2210.0" shows in the CENTER window
    0.5        "2210.5" shows in the CENTER window
    0.5        "2210.0" shows in the CENTER window
    ENTER      "2210.0" flashes, ENTER turns OFF
               The demodulator center frequency is set to 2210 Hz

Note:   When the center changes, the previous shift frequency  is �
maintained.  If previous MARK and SPACE were 1000.0 and 1200.0 Hz �
(Shift  = 200.0 Hz), setting center to 2210 Hz will maintain  200 �
Hz shift and change MARK to 2110.0 Hz and SPACE to 2310.0 Hz.

To save the new center frequency, the ENTER key must be pressed.
Š
7.2  MARK ONLY (2nd level):

Pressing 2ND then MARK enables the MARK ONLY demodulator mode and �
turns  ON  the MK ONLY indicator.  If the FSK indicator  was  ON, �
that indicator turns OFF.  If the SP ONLY indicator was on,  that �
indicator turns OFF.

    KEYS       ACTION
    -----      -------------------------------------------------
    2nd        Enable second level function
    MARK       Select demodulator MARK ONLY mode.
               Turn ON the MK ONLY indicator.

To save the new demodulator mode, the ENTER key must be pressed.


8.  SPACE ONLY KEY

The SPACE ONLY key has both a first and a second level function.

8.1  SPACE (first level):

Press SPACE alone to enter the SPACE filter frequency (channel 1) �
or  the  SPACE  transmit tone (channel  2)  when  the  MARK/SPACE �
display  mode is active.  The following example assumes that  the �
demodulator, channel 1, is selected.

    KEYS       ACTION
    -----      -------------------------------------------------
    SPACE       Blank the SPACE display window, ENTER turns ON
    2295       "2295.0" shows in the SPACE window
    ENTER      "2295.0" flashes, ENTER turns OFF
               The SPACE filter is set to 2295.0 Hz


When the display mode is set for CENTER/SHIFT, the SPACE key sets �
a new SHIFT frequency for the demodulator filters, channel 1,  or �
the  transmit  tones, channel 2.  The following  example  assumes �
that the demodulator, channel 1, is selected.

    KEYS       ACTION
    -----      -------------------------------------------------
    SPACE      Blank the SHIFT display window, ENTER turns ON
    200        " 200." shows in the SHIFT window
    ENTER      " 200." flashes, ENTER turns OFF
               The demodulator shift frequency is set to 200 Hz.

Note:   When the shift changes, the previous center frequency  is �
maintained.   If previous center and shift were 2210.0 and  170.0 �
Hz,  setting  shift  to 200 Hz will retain  the  2210  Hz  center �
frequency and change MARK to 2110.0 Hz and SPACE to 2310.0 Hz.

To save the new shift frequency, the ENTER key must be pressed.
Š
8.2  SPACE ONLY (2nd level):

Pressing 2ND then SPACE enables the SPACE ONLY demodulator mode and �
turns  ON  the SP ONLY indicator.  If the FSK indicator  was  ON, �
that indicator turns OFF.  If the MK ONLY indicator was on,  that �
indicator turns OFF.

    KEYS       ACTION
    -----      -------------------------------------------------
    2nd        Enable second level function
    SPACE      Select demodulator SPACE ONLY mode.
               Turn ON the SP ONLY indicator.

To save the new demodulator mode, the ENTER key must be pressed.


9.  DIV KEY

The DIV key toggles the demodulator diversity option ON and  OFF.  �
When ON, the DIV indicator turns ON.

    KEYS       ACTION
    -----      -------------------------------------------------
    DIV        Turn DIVERSITY option ON; turn ON DIV indicator
    DIV        Turn DIVERSITY option OFF; turn OFF DIV indicator

To save the new demodulator mode, the ENTER key must be pressed.


10.  MUTE KEY

The MUTE key toggles the modulator mute feature ON and OFF.  This �
feature  operates  correctly  only when  the  internal  modulator �
jumper is set for MUTE.  When the mute option is ON and  transmit �
data stops, the transmit tones are turned OFF with the PTT output �
after  the keyline delay expires.  The MUTE indicator is ON  when �
this  feature is enabled.  When the mute option is OFF,  the  PTT �
output and the transmit tones are always ON.

    KEYS       ACTION
    -----      -------------------------------------------------
    MUTE       Turn MUTE option ON; turn ON the MUTE indicator
    MUTE       Turn MUTE option OFF; turn OFF the MUTE indicator

To save the new mute setting, the ENTER key must be pressed.

.pa
11.  REMOTE KEY

The REMOTE key selects local and remote control of the  ST-8000A.  �
When  REMOTE  is enabled, the REMOTE indicator turns ON  and  all �
parameter control is via the rear panel remote control port.  The �
REMOTE LED is ON whenever Remote control is active.  When  remote �
control mode is enabled, all keypad keys are disabled except  for �
the REMOTE key.

Keypad or local control is restored by pressing the REMOTE key.  

    KEYS       ACTION
    -----      -------------------------------------------------
    REMOTE     Enable REMOTE control; turn ON REMOTE indicator
    REMOTE     Enable LOCAL control; turn OFF REMOTE indicator

The  local or remote control status is saved in the  non-volatile �
memory immediately; no ENTER key press is required.


12.  AMH HOLD KEY

The AMH HOLD key has both a first and a second level function.

12.1  AMH (first level):

The  AMH key toggles the Automatic Mark-Hold receive  feature  ON �
and OFF.  When AMH is ON, the AMH indicator is turned ON.

    KEYS       ACTION
    -----      -------------------------------------------------
    AMH        Turn AMH option ON; turn ON the AMH indicator
    AMH        Turn AMH option OFF; turn OFF the AMH indicator

To save the new AMH setting, the ENTER key must be pressed.


12.2  HOLD (2nd level):

Pressing  2ND  then HOLD toggles the MARK hold  feature  for  the �
selected  channel.  When channel 1 is selected,  the  demodulator �
output  is  held  in  the MARK  condition.   When  channel  2  is �
selected,  the  transmit tone output is held in the  MARK  state.  �
The HOLD indicator on the front panel shows the current state for �
the  selected  channel.  The following example assumes  that  the �
transmit channel 2 is selected.

    KEYS       ACTION
    -----      -------------------------------------------------
    2ND        Enable second level function
    HOLD       Turn HOLD option ON; turn ON the HOLD indicator
    2ND        Enable second level function
    HOLD       Turn HOLD option OFF; turn OFF the HOLD indicator

To save the new HOLD setting, the ENTER key must be pressed.Š
13.  NORM REV KEY

The NORM REV key has both a first and second level function.

13.1  NORM (first level):

The  NORM  key sets the selected channel polarity to  NORMAL  and �
turns OFF the REV indicator.

    KEYS       ACTION
    -----      -------------------------------------------------
    NORM       Enable NORMAL polarity; turn OFF REV indicator

To save the new polarity setting, the ENTER key must be pressed.


13.2  REV (2nd level):

Pressing  2ND  then  REV sets the selected  channel  polarity  to �
REVERSE and turns ON the REV indicator.

    KEYS       ACTION
    -----      -------------------------------------------------
    2ND        Enable second level function
    REV        Enable REVERSE polarity; turn ON REV indicator

To save the new polarity setting, the ENTER key must be pressed.


14.  SYNCH REGEN KEY

The SYNCH REGEN key has both a first and second level function.

14.1  SYNCH (first level)

The  SYNCH key toggles the clocked synchronous data mode  ON  and �
OFF.  When ON, the SYNC indicator turns ON and the modem  receive �
data  outputs are internally re-clocked with a recovered  mid-bit �
clock.   When  OFF, the SYNC indicator turns OFF  and  the  modem �
receive  data outputs are directly connected to  the  demodulator �
output.
.pa

When  the SYNC indicator turns OFF, the bit display  prompts  for �
the  receive data regeneration word length.  The current  setting �
is  shown,  and  it may be set to 5, 6, 7, or  8  bits.   If  the �
current setting is correct, ENTER only is pressed.

    KEYS       ACTION
    -----      -------------------------------------------------
    SYNCH      Enable SYNC mode; turn ON the SYNC indicator
               If REGEN mode was ON, it is turned OFF
    SYNCH      Disable SYNC mode; turn OFF the SYNC indicator
               "L=5 " is displayed in the BAUD window.
    8          "L=8 " is displayed in the BAUD window.
    ENTER      Flash the BAUD window and restore BAUD RATE
               The new configuration is saved immediately.


13.2  REGEN (2nd level)

Pressing  2ND  then REGEN toggles the receive  data  regeneration �
mode ON and OFF.  When ON, the REGEN indicator turns ON, the SYNC �
indicator  turns  OFF,  and data  characters  received  from  the �
demodulator are regenerated for the receive data outputs.

    KEYS       ACTION
    -----      -------------------------------------------------
    2ND        Enable second level function
    REGEN      Enable REGENERATION; turn ON the REGEN indicator
               If SYNCH mode was ON, it is turned OFF.
    2ND        Enable second level function
    REGEN      Disable REGENERATION; turn OFF the REGEN indicator

To save the regeneration mode, the ENTER key must be pressed.


15.  CHAN KEY

The CHAN key alternately selects channel 1 and channel 2 for  the �
front panel display and parameter entry.

    KEYS       ACTION
    -----      -------------------------------------------------
    CHAN       Display channel 1, the demodulator
    CHAN       Display channel 2, the modulator

To save the new channel selection, the ENTER key must be pressed.

.pa
16.  BAUD RATE KEY

Press BAUD RATE to enter the baud rate for the selected  channel.  �
If  channel 1 is selected, the BAUD RATE sets the  bandwidth  for �
the receive filters, the regeneration data rate, and the  receive �
data mid-bit clock center frequency.  When channel 2 is selected, �
the BAUD RATE loads the new synchronous transmit clock frequency.

    KEYS       ACTION
    ---------  -------------------------------------------------
    BAUD RATE  Blank the BAUD display window, ENTER turns ON
    110        " 110." shows in the BAUD window
    ENTER      " 110." flashes, ENTER turns OFF
               The BAUD RATE is set to 110 bits per second.


17.  CLEAR KEY

The  CLEAR key restores the last saved modem  parameter  settings �
whenever  the ENTER key indicator is flashing.  This key  may  be �
used  to restore the old MARK, SPACE, and BAUD RATE  settings  if �
CLEAR is pressed before ENTER as a new value is entered.